## Slide 1
CAD-DERIVED MODEL: SUPPORTED CONTROL
Abductor-enhanced control keeps the supported legs separated
1
80% vertical support · hybrid control · reference tensions · knee/contact assumptions
Notes: Recorded physics from D:/GitHub/Bipedal_Robot/Code/MuJoCo_SNS/robot_torso/runs/abd_defense_exact.npz. Model D:/GitHub/Bipedal_Robot/Code/MuJoCo_SNS/robot_torso/ah001_abduction_diagnostic_v2.xml. 75 kg; 54 reference-tension actuators, 262-neuron hybrid SNS/postural controller, 2 ms step. 80% actual vertical support after 15 s, with lateral and angular pelvis assistance. Provisional relative-knee passive stops and opposite-leg CAD contacts are active. Abductor control combines separation feedback and a 6% allocation floor on currently abducting routes; global activation floor is 5%. This is not independent balance, calibrated BPA force validation, or accepted walking. Foot toe-out remains. Detailed comparison is in the source assessment JSONs. Fresh reference and accelerated runs are bit-identical. The animation shows 20–32 s of the 40 s run. Right is blue, left gold, and selected hip-abducting routes are green.

## Slide 2
CAD-DERIVED MODEL: MEASURED COMPARISON
The matched control comparison quantifies leg separation
2
15–40 s interval | Off | On
Ankle order reversed | 67% | 0%
Minimum spacing | -38 mm | 142 mm
Right TFL activation | 22% | 82%
Vertical support | 80% | 80%
Abductor floor | 5% | 6%
All other conditions matched. Lateral and angular pelvis support remain active.
This supported diagnostic does not establish independent balance or BPA-controlled walking.
Notes: Recorded physics from D:/GitHub/Bipedal_Robot/Code/MuJoCo_SNS/robot_torso/runs/abd_defense_exact.npz. Model D:/GitHub/Bipedal_Robot/Code/MuJoCo_SNS/robot_torso/ah001_abduction_diagnostic_v2.xml. 75 kg; 54 reference-tension actuators, 262-neuron hybrid SNS/postural controller, 2 ms step. 80% actual vertical support after 15 s, with lateral and angular pelvis assistance. Provisional relative-knee passive stops and opposite-leg CAD contacts are active. Abductor control combines separation feedback and a 6% allocation floor on currently abducting routes; global activation floor is 5%. This is not independent balance, calibrated BPA force validation, or accepted walking. Foot toe-out remains. Detailed comparison is in the source assessment JSONs. Fresh reference and accelerated runs are bit-identical. The still is from 24.00 s. The ablation removes the extra separation gain and reduces the abductor floor to the 5% global floor. Other controls, geometry, constraints, support protocol, and initial pose are held fixed. Ankle order alone is not a full collision test; the mesh-contact and loop-closure audit is separate.