## Slide 1: Movement and Control of Biomimetic Humanoid Robots
Ben P. Bolen · PhD Defense
November 6, 2026
Notes: My dissertation develops ways to predict actuator force, compare robot joints with human torque targets, and test sensory control. The research robot serves as an experimental platform for studying how mechanics and neural control work together.
Sources: Portland State University · Agile & Adaptive Robotics Laboratory

## Slide 2
Robots on warehouse floors face different challenges from robots on rubble
Amazon Robotics; DARPA Robotics Challenge (2015)
Predictable contact
Changing contact and balance
2
Notes: Wheels work efficiently on prepared warehouse floors. Rubble introduces changing contacts and disturbances. These photographs motivate our interest in compliant legs and neural control; they are not a controlled comparison of the two robots.
Sources: Amazon Robotics; DARPA Robotics Challenge (2015)
https://www.aboutamazon.com/news/operations/amazon-robotics-headquarters-tour-westborough-massachusetts
https://newatlas.com/robotics/fast-two-legged-robots-roundup/

## Slide 3
Biomimetic robots let us test mechanics and neural control
Asano et al. (2016); Bolen and Hunt (2019); Dissertation Ch. 1
Biological mechanisms
Controlled robot experiments
3
Notes: Biology informs robot design, while biomimetic robots let us intervene in mechanics and neural pathways in ways that would be impossible in humans. Better prosthetic and orthotic devices are a later application. Kengoro illustrates physical biomimicry; the AARL leg is our research platform.
Sources: Asano et al. (2016); Bolen and Hunt (2019); Dissertation Ch. 1

## Slide 4
Four knowledge and tool gaps for biomimetic robot research
Dissertation Chs. 3–6
BPA characterization
How does length change force?
Joint design factors
What torque reaches the joint?
SADb
Which sensory evidence applies?
SNS tools
Which pathway causes the behavior?
4
Notes: Four questions organize the dissertation: what force an actuator can produce, how a real joint transmits it, where to find sensory evidence with its context, and how to test candidate neural mechanisms. SADb addresses the evidence-access question.
Sources: Dissertation Chs. 3–6

## Slide 5
BPA force depends on length, pressure, and contraction
Bolen et al., Actuators 15(5):230 · Hunt, INRC (2019), slide 49
Contracted
Uncontracted
5
Notes: Inflation changes the actuator’s length and diameter. The two photographs establish contracted and uncontracted states. Our rig measures force and pressure at controlled lengths. First, consider how resting length affects the maximum available force.
Sources: Bolen et al., Actuators 15(5):230 · Hunt, INRC (2019), slide 49

## Slide 6
Shorter BPAs deliver less maximum isometric force
Bolen et al. (2026), Actuators 15(5):230 · Dissertation Ch. 3
Resting length changes the force available to a robot design
6
Notes: At 620 kPa, shorter actuators produce less maximum force in both tested diameters. The manufacturer prediction has the opposite trend. Resting length therefore needs to enter the force model.
Sources: Bolen et al. (2026), Actuators 15(5):230 · Dissertation Ch. 3

## Slide 7
Resting-length scaling completes the normalized force model
Bolen et al., Actuators 15(5):230 · Dissertation Ch. 3
7
Notes: Both normalized force surfaces use the same pressure colors and symbol conventions. The legend identifies measured points, fitted curves, and manufacturer predictions. Multiplying normalized force by the resting-length force scale gives the complete model. The next slide shows its practical effect at 112 mm.
Sources: Bolen et al., Actuators 15(5):230 · Dissertation Ch. 3

## Slide 8
At 112 mm, the new model reduces force error to 4.5%
Bolen et al. (2026), Actuators 15(5):230 · Dissertation Ch. 3
Chart: Force, N
| Measured | New model | Manufacturer
Force (N) | 350.9 | 335.3 | 498.6
Absolute error (%) | 0 | 4.5 | 42.1
10 mm BPA · 112 mm resting length · 620 kPa
8
Notes: The measured force is 350.9 N, compared with 335.3 N from the new model and 498.6 N from the manufacturer. Bars use the force axis; diamonds use the right error axis. The published errors are 4.5% and 42.1%. These are prediction errors, not uncertainty intervals.
Sources: Bolen et al. (2026), Actuators 15(5):230 · Dissertation Ch. 3

## Slide 9
Length offsets, compliance, and wrapping change predicted joint torque
Dissertation Ch. 4 · Length correction and effective attachment mechanics
χ₀
Unloaded length offset
χ₁, χ₂
Effective system stiffness
χ₃
Wrapping length loss
9
Notes: Actuator force depends on usable muscle length. Chi-zero corrects an unloaded length offset. Chi-one and chi-two represent effective system stiffness, including fixtures and the loading path. Chi-three scales wrapping-related length loss. Held-out torque curves test the resulting model.
Sources: Dissertation Ch. 4 · Length correction and effective attachment mechanics

## Slide 10
Design corrections reduce error on held-out knee tests
Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4
Torque, N m
(C)
(D)
Knee angle, deg
Held-out mean RMSE: 7.588 to 1.490 N m
10
Notes: These are the held-out 46 cm and 40 cm-tendon flexor tests. The full model uses the shared effective stiffness pair. Its validation mean RMSE is 1.490 N m. With a better transmission model, we can redesign the route against a human torque target.
Sources: Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4

## Slide 11
The corrected model predicts a cam route with torque headroom
Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4
+30.83% above required envelope · 269–507 kPa predicted pressure
11
Notes: The adopted cam route predicts at least 30.83% margin above the required envelope, which includes 5% overshoot. The predicted pressure requirement is 269–507 kPa. The next comparison tests the built route.
Sources: Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4

## Slide 12
All nine cam-route measurements exceed the selected human target
Dissertation Ch. 4 · Physical extensor tests
Two 20 mm BPAs
9 of 9 human targets met
12
Notes: All nine extensor measurements exceed the selected human target. Keep the measured blue points separate from the pressure-specific and 620 kPa predictions. The point near −86.5° remains above the human target; its 2.06 N m discrepancy concerns the pressure-specific prediction.
Sources: Dissertation Ch. 4 · Physical extensor tests

## Slide 13
All fifteen flexor measurements meet the human target
Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4
15 of 15 targets met · 226.5–638 kPa · negative torque denotes flexion
13
Notes: All fifteen flexor measurements meet or exceed the selected human target from −119° to +5°. Flexion torque is negative, so compare magnitudes. The points establish isometric capacity, while the variable-pressure measurements and nominal prediction curve describe different conditions.
Sources: Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4

## Slide 14
SADb makes sensory evidence searchable and traceable
SADb Explorer · Offline snapshot: 1,393 records
Open offline SADb
Search · inspect · follow · compare
14
Notes: SADb retains experimental context when searching sensory evidence. Demonstrate search, record details, citation navigation, and pivot drill-through. The embedded walkthrough works offline. The link opens the full app. Table contains 1,393 records; Pivot and Bubble map use the 943-entry Papers category. External links and online search need a connection.
Sources: SADb Explorer · Offline snapshot: 1,393 records

## Slide 15
Suspended leg motion does not establish weight-bearing walking
1 · W2L walker and controller · Dissertation Table 6.1
Native recording pending
Suspended
Native recording pending
Released
15
Notes: Compare the original walker while suspended and after release. Leg motion alone does not establish weight-bearing behavior. This motivates tools that separate neural activity, sensory feedback, and mechanical support. Continue with the W2L feedback comparison.
Sources: AnimatLab walker · Original model and controller

## Slide 16
Sensory feedback changes bilateral foot-loading timing
1 · W2L walker and controller · Dissertation Table 6.1
Left leg: solid · Right leg: dashed
5
10
15
20
25
30
5
10
15
20
25
30
Time (s)
Time (s)
Feedback intact: 0.498 cycle
Feedback disabled: 0.223 cycle
16
Notes: With controller, drive, and support held fixed, sensory feedback changes median bilateral loading phase from 0.223 to 0.498 cycles. The supported-stepping criterion is 0.35–0.65. The result identifies a role for feedback in coordination.
Sources: Dissertation Ch. 6 · Fixed-controller sensory comparison

## Slide 17
Rhythmic Gait2392 cycles retain hip and knee errors
2 · Gait2392-based models · Dissertation Table 6.1
Hip timing differs
Knee timing differs
No fitted phase shift
or amplitude scaling
Gait cycle, %
10 cycles per leg · stance fractions 0.71 / 0.65 versus reference 0.61
17
Notes: The Gait2392 reference provides a second model comparison. Hip and knee traces expose differences that rhythmic cycles alone would miss. Preserve the source alignment and compare waveform, excursion, and timing. The complete eight-panel comparison is on question slide 39.
Sources: Dissertation Ch. 6 and Appendix D · Current saved verification records

## Slide 18
Graphical blocks close the loop between muscle mechanics and neurons
3 · SNS-Simscape blocks and editor · Dissertation Table 6.1
Ia feedback
Synaptic current
Motoneuron
Activation
BPA force
Muscle length and velocity return through the coupled model
18
Notes: The graphical library supplies the components for a sensory pathway: spindle output, synaptic current, a motoneuron, activation, and BPA force. The coupled mechanical model returns muscle length and velocity. The loaded-arm example tests whether such feedback changes a mechanical response.
Sources: SNS-Simscape library · Dissertation Table 6.1, third contribution

## Slide 19
Sensory feedback reduces sag in the loaded-arm model
3 · SNS-Simscape blocks and editor · Dissertation Table 6.1
B Feedback on/off
Sag: 2.00° with feedback · 7.85° without feedback
19
Notes: With feedback, the loaded arm sags 2.00°, compared with 7.85° without it. Biceps Ia excites its own motoneuron and inhibits the antagonist; own-muscle Ib is inhibitory. The circuit and the matched traces show the implemented feedback effect.
Sources: Dissertation Ch. 6 and Appendix D · Current saved verification records

## Slide 20
Extra abductor control prevents crossing in the AH001 test
4 · CAD-derived robot model · Dissertation Table 6.1
15–40 s | Off | On
Crossed states | 67% | 0%
Min. spacing | −38.3 mm | 142.4 mm
54 reference-tension actuators; 80% vertical + lateral/angular assistance
MN clamp cancels PF/reflex currents; regular stepping unverified
20
Notes: In the supported AH001 comparison, extra abductor control removes crossed states and increases minimum separation. The model uses reference tensions, 80% vertical assistance, lateral/angular support, and an MN clamp that cancels PF/reflex currents. This diagnostic does not establish accepted regular stepping. Question slide 33 collects the model assumptions.
Sources: Dissertation Ch. 6 and Appendix D · Current saved verification records

## Slide 21
The MuJoCo–Simulink bridge preserves measured signals
5 · MuJoCo–Simulink integration · Dissertation Table 6.1
SNS-Simscape
controller
MuJoCo
mechanical model
Activation
commands
Sensory
measurements
5 sensor channels · 80 scored steps · maximum deviation 0
21
Notes: The bridge exchanges activation commands and sensory measurements. In the saved interface test, all five sensor channels match the Python reference bit for bit over 80 scored steps. The displayed muscle-length traces show that agreement over 0.4 s. Controlled experiments then test the coupled behavior.
Sources: Dissertation Ch. 6 · Saved bridge sensor-readback test

## Slide 22
The tools make each of Hunt’s four training steps observable
6 · Curriculum and experiment drivers · Dissertation Table 6.1
1
Set intrinsic CPG rhythm
SNS blocks and open-loop traces
2
Train feedback → CPG
Afferent playback and timing
3
Train CPG/PF → MN
Motor-neuron peak comparisons
4
Refine Ia/Ib → MN
Closed-loop pathway tests
22
Notes: Hunt’s four steps specify where training acts: intrinsic rhythm, feedback to the CPG, CPG/PF output to motoneurons, and Ia/Ib feedback to motoneurons. The tools expose the activity and mechanical response needed to assess each step.
Sources: Hunt, INRC presentation (2019), slide 44 · Dissertation Ch. 6

## Slide 23
Two deleted bursts can preserve or reset the rhythm
7 · Literature circuits and variants · Dissertation Table 6.1
Stimulated layer | RG shift, cycles
RG | 0.211
PF | 0.000
MN | 0.000
RG: rhythm generator
PF: pattern formation
MN: motor neuron
Reduced Deng-derived circuit · two baseline periods · suspended model
23
Notes: The reduced Deng-derived circuit suppresses two expected motor bursts at each tested layer. RG stimulation shifts the clock by 0.211 cycle. PF and MN stimulation suppress output without resetting the RG clock. Read neural timing and motor output together when interpreting a deletion.
Sources: Dissertation Ch. 6 and Appendix D · Current saved verification records

## Slide 24
Researchers can connect source evidence to a tested actuator or pathway
Dissertation Chs. 3–7
Select an actuator
Test a route
Trace a sensory hypothesis
Test a pathway
24
Notes: These contributions enable research decisions: select an actuator, test a route against a target, recover the context for a sensory hypothesis, and test the corresponding pathway. Each step has an identifiable source and an observable outcome.
Sources: Dissertation Chs. 3–7

## Slide 25
The next experiments must transfer the models to loaded robot movement
Dissertation Discussion · Future work enabled
Dynamic loading and physical transfer
Graded support reduction
25
Notes: The next experiments add dynamic loading to the hardware, reduce support in controlled stages, and transfer specified feedback mechanisms to the robot. These experiments address movement in unstructured environments and the use of robots to study biological hypotheses.
Sources: Dissertation Discussion · Future work enabled

## Slide 26
The dissertation makes actuator, route, and feedback choices testable
Dissertation Conclusion
Predict force
Meet selected torque targets
Ground sensory hypotheses
Test neural mechanisms
Thank you · Questions
26
Notes: The dissertation makes actuator, route, and feedback choices testable. It supplies force characterization, joint design factors with physical target comparisons, a sensory evidence resource, and tools for controlled neural–mechanical experiments. Thank the committee and audience.
Sources: Dissertation Conclusion

## Slide 27
SADb keeps experimental context beside the proposed robot interpretation
Dissertation Ch. 5 · Focus record and connected sources
Source and
experimental context
Robot interpretation
to test
27
Notes: One SADb record keeps source context beside the proposed robot interpretation. The interpretation is a hypothesis to test. Connected sources help check that interpretation before selecting a pathway or parameter.
Sources: Dissertation Ch. 5 · Focus record and connected sources

## Slide 28
Joint torque depends on force direction and moment arm
Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4
O
p
r
F
r⊥
τz = (r × F) · ẑ
|τz| = F r⊥
Routing also changes
actuator length
A force model needs a transmission model to predict delivered torque
28
Notes: Torque follows the cross product of the attachment position and tensile force. Its magnitude is force times perpendicular moment arm. Changing a route also changes actuator excursion, so moment arm alone is insufficient.
Sources: Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4

## Slide 29
The model workflow supports distinct mechanical implementations
Dissertation Ch. 6, Model construction and neural-controller interfaces
Command exchange, circuit agreement, and motion each require their own check
29
Notes: The workflow separates CAD/Simscape construction from OpenSim/MuJoCo conversion. Controllers can use graphical SNS blocks or SNS-Toolbox. Each implementation needs component, interface, and coupled-model checks.
Sources: Dissertation Ch. 6, Model construction and neural-controller interfaces

## Slide 30
Staged tests separate rhythm, feedback, and mechanical support
Dissertation Ch. 6, curriculum Table 6.2
Condition introduced | Question tested
Suspended, without sensory feedback | Can the circuit generate activity?
Sensory feedback | How does feedback reshape the output?
Standing and perturbations | Can the model maintain posture?
Supported ground contact | Does physical coordination meet the criterion?
Reference and intervention comparisons | Which mechanism or mismatch explains the result?
30
Notes: The curriculum introduces feedback, perturbations, and mechanical demands in stages. Each stage asks a different question. Passing a rhythm test does not establish performance at the later mechanical stages.
Sources: Dissertation Ch. 6, curriculum Table 6.2

## Slide 31
Matched rhythm cores reproduce the same driven bursts
Dissertation Ch. 6 and Appendix D · Current saved verification records
1.000 s period · 10 expected bursts · correlation ≥ 0.99996
31
Notes: Under the matched phasic-drive protocol, both implementations produce the ten expected bursts with a 1.000 s period and correlation of at least 0.99996. Removing those phasic inputs latches both. The result establishes agreement for this defined core and protocol.
Sources: Dissertation Ch. 6 and Appendix D · Current saved verification records

## Slide 32
The knee model produces a transient sensory response
Dissertation Ch. 6 and Appendix D · Current saved verification records
2 nA for 30 ms
1.09° at 111 ms
Recovery at 6.355 s
Six neural saturation widths changed in this configuration
32
Notes: The knee example applies 2 nA for 30 ms after settling. The response peaks at 1.09° at 111 ms and meets the recovery thresholds at 6.355 s. Six neural saturation widths changed. This is an engineering demonstration of the implemented blocks.
Sources: Dissertation Ch. 6 and Appendix D · Current saved verification records

## Slide 33
The evidence establishes specific capabilities within clear limits
Current manuscript Ch. 6 / Appendix D · Session 1 AH001 records
Evidence level | What the result establishes | Remaining boundary
Measured hardware | Isometric torque capacity | Dynamic response and transfer
Neural demonstrations | Specified response and intervention effect | Circuit- and protocol-specific
Supported W2L / human models | Coupling and coordination tests | External support remains
AH001 integration | Hybrid allocation; PF/reflex currents cancelled | 80% vertical + lateral/angular support
AH001: reference tensions, MN clamp, provisional feet, and ideal brackets
No harness-free walking has been demonstrated
33
Notes: The hardware demonstrates isometric capacity. Neural interventions demonstrate responses under their specified protocols. Supported models test coupling and coordination. AH001 retains the stated support, reference tensions, provisional feet, ideal brackets, and hybrid clamp. No harness-free walking has been demonstrated.
Sources: Current manuscript Ch. 6 / Appendix D · Session 1 AH001 records

## Slide 34
The adopted identification reserves tests in each configuration
Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4
Configuration | Training | Held out | Not used
Pinned flexor | 2 | 2 | 1
Pinned extensor | 3 | 3 | 3
Shared effective stiffness pair: χ₁ = 39.98, χ₂ = 14.73 kN/m
34
Notes: The adopted flexor fold has two training tests, two held-out tests, and one unused test. The extensor fold has three in each category. Both configurations share the effective stiffness pair. These fitted terms aggregate system compliance.
Sources: Dissertation Ch. 4 · Current knee-torque manuscript, §§3–4

## Slide 35
Physical dimensions differ from prediction settings
Torque manuscript, Physical Tests · Dissertation Appendix C dimensions
Actuator | Resting length, mm | Tendon length, mm
Flexor 1 | 561 | 28
Flexor 2 | 560 | 30
Extensor 1 | 828 | 92
Extensor 2 | 826 | 85
Prediction inputs: flexor 561.49 / 5.00 mm; extensor 827.74 / ≈92.49 mm
35
Notes: These rows contain measured resting and tendon lengths. Prediction settings differ and remain identified separately. In particular, retain the nominal 562 mm prediction label rather than replacing it with a measured length.
Sources: Torque manuscript, Physical Tests · Dissertation Appendix C dimensions

## Slide 36
Stimulation duration changes the deletion interpretation
stimulus_results_all.csv · Current Appendix D layer-stimulus protocols
Protocol | RG shift, cycles | Motor shift, cycles
RG, two periods | 0.211 | 0.211
PF, two periods | 0.000 | 0.000
MN, two periods | 0.000 | 0.000
PF, one second | 0.000 | 0.208
36
Notes: Stimulus duration matters. The two-period PF pulse gives a non-resetting deletion, while a one-second PF control shifts motor timing by 0.208 cycle with no RG shift. Motor phase alone cannot identify an RG reset.
Sources: stimulus_results_all.csv · Current Appendix D layer-stimulus protocols

## Slide 37
AH001 separation control changes a matched diagnostic
AH001_20261028/PLACEMENT_RECOMMENDATION.md · asset_provenance.json
15–40 s measure | Control off | Control on
Reversed ankle ordering | 67% | 0%
Minimum separation | −38.3 mm | 142.4 mm
Right TFL mean activation | 22.3% | 81.8%
Vertical assistance | 80% BW | 80% BW
Sampled opposite-leg penetration | 2.700 mm | 0 mm
37
Notes: The matched AH001 interval is 15–40 s. The control bundle changes separation feedback and the activation floor on currently abducting routes. Reversed ankle ordering and sampled opposite-leg penetration are distinct measurements. Support remains the same.
Sources: AH001_20261028/PLACEMENT_RECOMMENDATION.md · asset_provenance.json

## Slide 38
Reported force comparisons favor the model in the shown cases
Bolen et al. (2026), Actuators 15(5):230 · Dissertation Ch. 3
Measured-versus-predicted force at the two displayed actuator lengths
38
Notes: The diagonal indicates equality between measured and predicted force. Preserve the model identities and the two tested lengths. These source panels compare the reported cases.
Sources: Bolen et al. (2026), Actuators 15(5):230 · Dissertation Ch. 3

## Slide 39
The complete IK overlay also exposes contact differences
Dissertation Ch. 6 and Appendix D · Current saved verification records
Model mean and standard deviation · OpenSim IK reference
39
Notes: The full IK figure adds ankle and stance comparisons. Each leg is aligned independently to loading onset, without fitted phase or amplitude adjustments. Separate leg alignment does not establish bilateral phase agreement.
Sources: Dissertation Ch. 6 and Appendix D · Current saved verification records

## Slide 40
The saved AH001 replay shows supported hybrid motion
AH001_20261028/asset_provenance.json · saved 20–32 s interval
Optional 12-second replay · same supported-control diagnostic
40
Notes: Play the saved 20–32 s AH001 interval if useful. It illustrates the same supported hybrid-control condition. Use slide 33 for its assumptions and slide 37 for the matched diagnostic measures.
Sources: AH001_20261028/asset_provenance.json · saved 20–32 s interval

## Slide 41
Changing neural encoding changes rhythm timing
7 · Literature circuits and variants · Dissertation Table 6.1
0.399 s non-spiking → 0.621 s spiking · 55.6% longer
41
Notes: For the saved constant-drive comparison, changing from non-spiking to spiking encoding increases the period from 0.399 s to 0.621 s, or 55.6%. The panels use different readouts. The comparison shows timing sensitivity to encoding choice.
Sources: Dissertation Appendix D · Graded and spiking comparisons